## Slide 1
INTELLIGENT TRAFFIC SIGNAL
CONTROLLER
With Pedestrian Input & Emergency Override
Embedded Systems Design (ESD) & Internet of Things (25EC2206E)
NUCLEO-F103RB • GPIO • TIM2 • EXTI/NVIC • UART
Team members :
251008001 - Yeswanth
2510080012 - Sai Vignesh
2510080022 - Niharika
2510080049 - Tejaswini
2510080054 - Krithik Reddy
2510080011 - Srujan Reddy
2510080056 - Ruthvik Yerram
KLEF | AI & DS

## Slide 2
INTELLIGENT TRAFFIC SIGNAL CONTROLLER
Problem Statement & Objectives
ESD & IoT • Project Based Learning
02
A traffic controller must sequence signals safely while responding to asynchronous inputs.
NORMAL SEQUENCE
RED → GREEN → YELLOW
Target: 5 s / 5 s / 2 s
PEDESTRIAN REQUEST
Capture a button press and serve it at a safe point.
EMERGENCY OVERRIDE
Prioritize the emergency event and command a safe output.
• Configure GPIO outputs for the three traffic LEDs.
• Use a hardware timer and finite-state machine instead of blocking delays.
• Integrate EXTI/NVIC, an IR vehicle sensor, relay output and UART status.

## Slide 3
INTELLIGENT TRAFFIC SIGNAL CONTROLLER
Hardware Platform
ESD & IoT • Project Based Learning
03
The supplied report identifies the photographed board as NUCLEO-F103RB.
• STM32F103RB microcontroller board
• Breadboard, jumper wires and current-limited LEDs
• Push button for pedestrian input
• Digital IR sensor for vehicle-presence detection
• Relay module for simulated emergency output
• USB connection for power and programming
Photo evidence confirms physical assembly; exact pin mapping must come from the CubeMX .ioc file.

## Slide 4
INTELLIGENT TRAFFIC SIGNAL CONTROLLER
System Architecture
ESD & IoT • Project Based Learning
04
Pedestrian
Button
IR Vehicle
Sensor
Emergency
Input
STM32F103RB
Finite-State Machine
TIM2 + EXTI / NVIC
RED / YELLOW / GREEN LEDs
Emergency Relay
UART Status / Logging
Inputs → event capture → control decision → outputs

## Slide 5
INTELLIGENT TRAFFIC SIGNAL CONTROLLER
Finite-State Machine
ESD & IoT • Project Based Learning
05
RED
5 seconds
GREEN
5 seconds
YELLOW
2 seconds
RED
repeat
PEDESTRIAN EVENT
Latch request; serve at a safe RED boundary.
EMERGENCY EVENT
Override normal timing; proposed safe pattern is all-red + relay.
The timing values are design targets, not measured results in the supplied evidence.

## Slide 6
INTELLIGENT TRAFFIC SIGNAL CONTROLLER
Timer-Based Signal Timing
ESD & IoT • Project Based Learning
06
Target cycle: 5 s RED + 5 s GREEN + 2 s YELLOW = 12 seconds
RED
5s
GREEN
5s
YELLOW
2s
TIMER FORMULA
f_update = f_timer / [(PSC + 1) × (ARR + 1)]
ILLUSTRATIVE 1 ms TICK
If TIM2CLK = 72 MHz: PSC = 7199, ARR = 9
Important: verify the actual RCC/APB timer clock in CubeMX before using these values.

## Slide 7
INTELLIGENT TRAFFIC SIGNAL CONTROLLER
Inputs, Interrupts & Emergency Handling
ESD & IoT • Project Based Learning
07
EXTI — PEDESTRIAN
Button edge is captured promptly. ISR sets a pending flag; main logic decides when it is safe to serve.
IR SENSOR
Digital input indicates object present/absent. Confirm polarity and 3.3 V compatibility.
EMERGENCY
Highest-priority event. Proposed response: all-red traffic output and relay activation.
Interrupt design principles
• Keep ISRs short: record events, then return.
• Avoid blocking delays and UART transmission inside interrupts.
• Use one output-update function to preserve safe lamp combinations.

## Slide 8
INTELLIGENT TRAFFIC SIGNAL CONTROLLER
Implementation Workflow
ESD & IoT • Project Based Learning
08
Configure GPIO
Test each LED independently
1
Configure TIM2
Verify tick with counter/debug output
2
Build FSM
Check RED → GREEN → YELLOW
3
Add EXTI
Latch and debounce button events
4
Integrate modules
IR, relay, UART and event priority
5
Validate
Capture timing and functional evidence
6
Recommended test order: outputs first, timer second, integrated events last.

## Slide 9
INTELLIGENT TRAFFIC SIGNAL CONTROLLER
Prototype & Observed Evidence
ESD & IoT • Project Based Learning
09
Observed: physical NUCLEO-F103RB setup; red and green LEDs illuminated in separate photos.
Photos do not independently prove exact timing, EXTI/NVIC behavior, UART output or relay contact actuation.
RED LIGHT
GREEN LIGHT

## Slide 10
INTELLIGENT TRAFFIC SIGNAL CONTROLLER
Results: What Is Verified vs. Pending
ESD & IoT • Project Based Learning
10
OBSERVED / SUPPORTED
• Hardware assembled and powered
• Red LED visibly illuminated
• Green LED visibly illuminated
NEEDS VERIFICATION
• 5 / 5 / 2 s timing trace
• Pedestrian EXTI and debounce
• IR detection polarity and response
• Relay contact switching and UART log
Evidence standard
• Use timestamped UART logs or an oscilloscope/logic analyzer for timing.
• Test emergency preemption while a normal state is active.
• Complete the actual pin map from the project .ioc file.

## Slide 11
INTELLIGENT TRAFFIC SIGNAL CONTROLLER
Conclusion
ESD & IoT • Project Based Learning
11
Key takeaway
A timer-driven finite-state machine provides a structured foundation for responsive, event-driven traffic control.
Educational prototype only — not intended for deployment on public roads.
THANK YOU